Dead reckoning with a gyro
David Grayson 2019-08-11

---
L3GD20H gyro
MinIMU-9 v3 Gyro, Accelerometer,
and Compass
(L3GD20H and LSM303D Carrier)

---
Angle estimation
- Read gyro regularly
- Multiply reading by time since last reading
- Add that to the robot’s angle estimate
  - angle += (gyro reading) × time

---
Position estimation
For every forward encoder tick, do:
  - x += cos(angle)
  - y += sin(angle)
For every reverse encoder tick, subtract.

---
L3GD20H characteristics

---
Zero-rate calibration
- At rest, my average reading was around
  5 to 15 (0.4 to 1.1 dps), depending on temperature.
- At startup, take 1000 readings, 2 ms apart.
- Store all the readings!
- Subtract zero-rate readings from subsequent readings.

---
Effect of zero-rate calibration
- Drift before: 46° per minute
- Drift after calibration: 1.3° per minute
  - (changes each time I reset)
- Comparison: 1 lsb = 0.07°/s = 4.2° per minute
- Comparison: 125″ × sin(1.3°) = 2.8″

---
First tests
two straight parts look
good individually,
but are not parallel!
log_190728_1.csv

---
Scale calibration
log_190730_2.csv

---
Scale calibration – angle vs time
log_190730_2.csv

---
Scale calibration results (counter-clockwise)
Avg angle	Expected angle	Error	Change in error
23725	23725	0
-9412	-9043	-369	-369
23004	23725	-721	-352
-10140	-9043	-1097	-376
22211	23725	-1514	-417
-10920	-9043	-1877	-363
21382	23725	-2343	-466
-11720	-9043	-2677	-334
20620	23725	-3105	-428
-12519	-9043	-3476	-371
19843	23725	-3882	-406
-13339	-9043	-4296	-414
19001	23725	-4724	-428
-14147	-9043	-5104	-380
18162	23725	-5563	-459
-15017	-9043	-5974	-411
17291	23725	-6434	-460
-15827	-9043	-6784	-350
16507	23725	-7218	-434
-16662	-9043	-7619	-401
15628	23725	-8097	-478
180 degrees CCW	= 32768
Average change in error	= −404.85
Correction factor	= 1.012355042

---
Scale calibration results (clockwise)
Avg angle	Expected angle	Error	Change in error
-25599	-25599	0	0
6891	7169	-278	-278
-26124	-25599	-525	-247
6429	7169	-740	-215
-26620	-25599	-1021	-281
5860	7169	-1309	-288
-27168	-25599	-1569	-260
5300	7169	-1869	-300
-27772	-25599	-2173	-304
4708	7169	-2461	-288
-28326	-25599	-2727	-266
4112	7169	-3057	-330
-28954	-25599	-3355	-298
3573	7169	-3596	-241
-29484	-25599	-3885	-289
2983	7169	-4186	-301
-30093	-25599	-4494	-308
2366	7169	-4803	-309
-30674	-25599	-5075	-272
1788	7169	-5381	-306
-31225	-25599	-5626	-245
180 degrees CW	= −32768
Average change in error	= −281.3
Correction factor	= 0.991415405

---
Effect of counter-clockwise scale calibration
After
Before

---
Log from
the contest

---
Future work
- Use a lower full-scale range for the gyro
- Use gyro’s FIFO
- Better zero-rate calibration
- Try scale calibration with encoder-only algorithm.