USB
Part 1: Wires, packets, transactions
David Grayson
2015-07-23

---
Which USB are we talking about?
- Full speed (12 Mbps)
- Universal Serial Bus Specification
  Revision 2.0, April 27, 2000
- 650 page document
- Engineering Change Notices (ECNs)

---
Types of USB
- Low Speed:	1.5 Mbps
- Full Speed:	12 Mbps
- High Speed:	480 Mbps
- SuperSpeed:	up to 5000 Mbps
- SuperSpeed+:	up to 10000 Mbps

---
Bus topology
- One host
  - Detects devices, initiate communication
- Multiple devices
  - Provides one or “functions” to the host

---
USB 2.0 section 4.1.1

---
Topology is enforced by connectors
A receptacle
B receptacle
B plug
A plug
http://uk.farnell.com/multicomp/mc32593/usb-2-0-type-a-recetpacle-th/dp/1696534

---
Prohibited cable assemblies
“USB is optimized for ease of use. The expectation is that if the device can be plugged in, it will work.”
USB 2.0 section 6.4.4

---
Prohibited cable assembly:
Extension cables assembly
USB 2.0 section 6.4.4
http://www.amazon.com/Belkin-USB-Extension-Cable-10-Feet/dp/B00001ZWXA

---
Prohibited cable assembly:
Cable that violates USB topology rules
But USB On-the-go (OTG) is fine.
USB 2.0 section 6.4.4	http://www.showmecables.com

---
Prohibited cable assembly:
Standard detachable cables for
low-speed devices
“Using a long high-/full-speed cable exceeds the capacitive load of low-speed.”
https://learn.adafruit.com/introducing-trinket/introduction
https://www.sparkfun.com/products/9825

---
- Chapter 6 has more mechanical specifications
- My favorite part:
7.9 lbs
2.2 lbs
USB 2.0 section 6.7

---
That's enough mechanical stuff.
Let's talk about the electronics….

---
USB wires
USB 2.0 section 6.3

---
Power distribution: Voltage
Devices typically get 5.0 V but it could be as low as 4.35 V.
USB 2.0 section 7.2

---
Current limits
- “Unit load” is defined to be 100 mA
- Low power device: 1 unit load (100 mA)
- High power device: up to 5 unit loads (500 mA)
- Devices cannot draw more than 1 unit load until the device is configured by the host.
- (Later USB specifications allow for a lot more current.)
- Suspend mode: 2.5 mA
USB 2.0 section 7.2.1, Suspend Current ECN

---
Sourcing VBUS
“No device shall supply (source) current on VBUS at its upstream facing port at any time.”
Arduino Uno does it though
http://forum.pololu.com/viewtopic.php?f=3&t=3083
USB 2.0 section 7.2.1

---
Inrush current limiting
VBUS
VBUS (5 V)
+++
+++
- - -
- - -
GND (0 V)
GND
USB Host
USB Device
120 µF < CHPB
1 µF < CRPB < 10 µF
USB 2.0 section 7.2.4.1; Device Capacitance ECN

---
USB data lines

---
USB resistors
D+ pull-up should be controllable so you can disconnect from the bus.
D+ pull-up should only be powered when VBUS is present.
D+ and D- use 0 V to 3.3 V signalling levels.
USB 2.0 figure 7-20; Pull-up/pull-down resistors ECN

---
Signalling levels
- J: D+ high, D- low: default
- K: D+ low, D- high
- SE0: both low: signals reset or end of packet
- SE1: both high: not used
USB 2.0 section 7.1.7.1

---
Packet boundaries
- Start of packet:
  Data lines switch from idle (J) to K.
- End of packet:
  SE0 for 2 bit times, J for 1 bit time.
USB 2.0 section 7.1.7.1

---
Sync pattern
Every packet starts with KJKJKJKK:
D+
USB 2.0 section 7.1.1.10

---
NRZI: Non Return to Zero Invert
- Changing voltage level represents a 0
- Same voltage level represents a 1
K J K J K J K K J J J K K J J K J K K J K K K J SE0
  -------- sync --------- 0 1 1 0 1 0 1 0 0 0 1 0 0 1 1 0
USB 2.0 section 7.1.8

---
Bit stuffing
A zero is inserted after every six consecutive ones in the data stream, to force a transition.
00101111110110110
USB 2.0 section 7.1.9

---
That's how packets work.
Now we can just think of each packet as a sequence of 0s and 1s.
Start, 0111011010111010101110000, End

---
Packet identifier (PID)
Every packet starts with a 4-bit PID and its inverse.
USB 2.0 section 8.3.1

---
PID types (the important ones)
- 0001: OUT token
- 1001: IN token
- 0101: SOF token
- 1101: SETUP token
- 0011: DATA0
- 1011: DATA1
- 0010: ACK handshake
- 1010: NAK handshake
- 1110: STALL handshake
USB 2.0 section 8.3.1

---
Packet types and their fields
- OUT, address, endpoint, CRC5
- IN, address, endpoint, CRC5
- SOF, frame number, CRC5
- SETUP, address, endpoint, CRC5
- DATA0, data, CRC16
- DATA1, data, CRC16
- ACK
- NAK
- STALL
address: 7-bit
endpoint: 4-bit
data: 0 to 1024 bytes

---
Packets are combined to form
transactions.

---
OUT transaction
Transfers data out from the host to the device
Host: OUT (address, endpoint)
Host: DATA0 or DATA1 packet
Device: ACK, NAK, STALL

---
IN transaction
Transfers data in to the host from the device
Host: IN (address, endpoint)
Device: DATA0, DATA1, or NAK packet
Host: ACK

---
USB 2.0 figure 8-38

---
Transaction considerations
- Host initiates all transactions
- Device must respond very fast
- Device responses are usually queued up ahead of time an then handled entirely by hardware
- Can't easily make wireless USB

---
Data toggle and error handling
- We already have ACK packets, but what happens if the ACK is lost?
- The sender must resend packet until ACKed.
- Receiver must be able to detect duplicate packets.
- Solution: data toggle bit included with every DATA packet in the PID (DATA0 or DATA1)
USB 2.0 section 8.6

---
Endpoint types
- Interrupt: guaranteed latency
- Bulk: best effort
- Control: requests and responses
- Isochronous: streaming, no error handling

---
EOP

---
USB 2.0 page 1

---
Address and endpoint fields
- Only present for OUT, IN, and SETUP packets
- 7-bit device address
  - Devices use address 0 after being reset (D+ and D- low for a while), and then the host assigns another address.
- 4-bit endpoint number
USB 2.0 section 8.3.2.1

---
Data field
- Only present for DATA0 and DATA1 packets.
- Integral number of bytes from 0 to 1024
USB 2.0 section 8.3.4

---
Cyclic Redundancy Checks (CRCs)
- 5-bit CRC for IN/OUT/SETUP packets.
- 16-bit CRC for DATA0/DATA1 packets.
- Packets with failed CRCs must be ignored.
USB 2.0 section 8.3.5